## Slide 1: MTS-417 Intro to Robotics LAB No. 1 Introduction to CoppeliaSim EDU
Lab Prepared by:
LE Hamza Sohail
Fall 2025 – DE 44 MTS
Department of Mechatronics Engineering, National University of Sciences and Technology, College of E&ME

## Slide 2: Lab Ethics
Just be disciplined and respectful…
Discipline includes the following:
  Time management
  Respecting peers, staff, faculty, and everyone
  Turning off computers at the end of Lab.
Participation is highly encouraged and Graded as well.
Eatables are not allowed in lab.

## Slide 3: Mechatronics

## Slide 4: Robots

## Slide 5: Fields in Robotics

## Slide 6: Robot Operating Systems (ROS)

## Slide 7: Linux vs Windows

## Slide 8: ROS Versions & Ubuntu

## Slide 9: CoppeliaSim EDU Let’s Start ! ! !

## Slide 10: Learning Objectives LAB 1
Understand CoppeliaSim EDU interface and scene hierarchy
Learn world vs local frame
Add, move, and simulate objects
Write and attach Lua child scripts
Move an object using a mathematical function
Introduce vector subtraction
Compute Euclidean distance between robot and goal
Use dot product to measure robot alignment with goal

## Slide 11: Learning Objectives LAB 1
Relate linear and angular velocity to robot motion
See how equations define motion (linear, oscillatory, circular, spiral) and Implement these equations in CoppeliaSim EDU 4.7

## Slide 12: Theory (World vs Local Frames)
World frame: fixed global reference
Local frame: attached to each object, moves with it
Robots operate in local frames; positions shown in world frame

## Slide 13: COPPELIASIM EDU 4.7
Open CoppeliaSim 4.7 EDU
Add a cube, sphere, and cylinder; rename in Scene Hierarchy
Move, rotate, and scale objects
Run simulation and observe gravity

## Slide 14: Linear Motion
Equation: x(t) = v · t
Insert a Cuboid
Attach a non-threaded child script
Modify script to move the cube with a sine function

## Slide 15: Linear Motion
Equation: x(t) = v · t
function sysCall_init() cube = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local t = sim.getSimulationTime() local v = 0.1 -- m/s local x = v * t sim.setObjectPosition(cube, -1, {x, 0, 0}) end

## Slide 16: Oscillatory Motion
Equation: x(t) = A sin(ωt)
function sysCall_init() cube = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local t = sim.getSimulationTime() local A = 0.5 local x = A * math.sin(t) -- oscillates ±0.5 sim.setObjectPosition(cube, -1, {x, 0, 0}) end

## Slide 17: Circular Motion
Equations: x(t) = R cos(ωt), y(t) = R sin(ωt)
function sysCall_init() cube = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local t = sim.getSimulationTime() local R = 0.5 local x = R * math.cos(t) local y = R * math.sin(t) sim.setObjectPosition(cube, -1, {x, y, 0}) end

## Slide 18: Spline Motion
Equations: x(t) = R(t) cos(ωt), y(t) = R(t) sin(ωt), R(t) = k·t
function sysCall_init() cube = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local t = sim.getSimulationTime() local k = 0.05 local R = k * t local x = R * math.cos(t) local y = R * math.sin(t) sim.setObjectPosition(cube, -1, {x, y, 0}) end

## Slide 19: Distance to Goal
Introduce vector subtraction
Compute Euclidean distance between robot and goal
Place Pioneer_p3dx robot
Place a cube at (2,2) as the goal
Attach a Lua script to compute distance

## Slide 20: Distance to Goal
function sysCall_init() robot = sim.getObjectHandle('Pioneer_p3dx') goal = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local rPos = sim.getObjectPosition(robot,-1) local gPos = sim.getObjectPosition(goal,-1) local dx = gPos[1] - rPos[1] local dy = gPos[2] - rPos[2] local dist = math.sqrt(dx*dx + dy*dy) print(string.format("Distance to goal: %.2f m", dist)) end

## Slide 21: Heading Alignment (Dot Product)
Use dot product to measure robot alignment with goal
Use Pioneer_p3dx at origin
Place goal at (2,2)
Compute dot product b/w heading and goal vector

## Slide 22
function sysCall_init() robot = sim.getObjectHandle('Pioneer_p3dx') goal = sim.getObjectHandle('Cuboid') end function sysCall_actuation() local rPos = sim.getObjectPosition(robot,-1) local gPos = sim.getObjectPosition(goal,-1) local ori = sim.getObjectOrientation(robot,-1)
  -- ori[1] = alpha (rotation around X-axis) → Roll
  -- ori[2] = beta (rotation around Y-axis) → Pitch
  -- ori[3] = gamma (rotation around Z-axis) → Yaw local theta = ori[3]
-- Robot heading vector local vx = math.cos(theta) local vy = math.sin(theta) -- Goal direction vector local dx = gPos[1] - rPos[1] local dy = gPos[2] - rPos[2] -- Dot product local dot = vx*dx + vy*dy print(string.format("Dot product = %.2f", dot)) end

## Slide 25
function sysCall_init()
robot = sim.getObjectHandle('Pioneer_p3dx')
goal = sim.getObjectHandle('Cuboid')
end
function sysCall_actuation()
local rPos = sim.getObjectPosition(robot,-1)
local gPos = sim.getObjectPosition(goal,-1)
local theta = sim.getObjectOrientation(robot,-1)[3]
local vx, vy = math.cos(theta), math.sin(theta)
local dx, dy = gPos[1]-rPos[1], gPos[2]-rPos[2] --This vector points from the robot toward the goal
local d = math.sqrt(dx*dx + dy*dy)
local dot = vx*dx + vy*dy -- = d cos(phi)
local cross = vx*dy - vy*dx -- = d sin(phi)
local phi = math.atan2(cross, dot) -- (-pi, pi]
print(string.format("d=%.3f dot=%.6f cross=%.6f cos?=%.3f sin?=%.3f ?=%.1f?",
d, dot, cross, dot/d, cross/d, math.deg(phi)
))
end --Significance: phi is the smallest rotation angle to face the goal exactly:

## Slide 26: Unicycle Kinematics
Relate linear and angular velocity to robot motion
Place Pioneer_p3dx
Write Lua to move at constant v
Add ω for circular motion and convert (v, ω) to wheel speeds

## Slide 27
function sysCall_init() leftMotor = sim.getObjectHandle('Pioneer_p3dx_leftMotor') rightMotor = sim.getObjectHandle('Pioneer_p3dx_rightMotor') r = 0.0975/2 -- wheel radius L = 0.33 -- axle length end function sysCall_actuation() local v = 0.2 -- linear velocity local w = 0.2 -- angular velocity local vL = (2*v - w*0.33)/(2*0.04875) local vR = (2*v + w*0.33)/(2*0.04875) sim.setJointTargetVelocity(leftMotor, vL) sim.setJointTargetVelocity(rightMotor, vR) end